## Slide 1: Ch.4. Groundwater
Recharge in Arid Region
  Evaporation is significant, which can make a big enrichment in isotopic compositions
  Evaporative enrichment in alluvial groundwater
Fig. 4-8 The isotopic composition of wadi runoff for three rainfall events in northern Oman. The regression lines for the summer rains (slopes indicated) show strong evaporation trends at humidities less than 50%. The local water line for northern Oman (NOMWL) is defined as d2H = 7.5 d18O + 16.1.

## Slide 2
Fig. 4-9 Deep groundwaters from fractured carbonate aquifers and shallow alluvial groundwaters in northern Oman. Alluvial groundwaters have experienced greater evaporative enrichment. Also shown is the average evaporation slope (s = 4.5) for the region, with h = 0.5.
the kinetic fractionation factors using Gonfiantini’s equations in Chapter 2, giving De18Ov-bl = –7.1‰ and De2Hv-bl = –6.3‰.
(etotal = ev-l + Dev-bl) for evaporation under these conditions, for the mean annual temperature of 30°C (and ev-l Table 1-4), are then –16.0‰ for 18O and –78‰ for 2H.
d18Ogw – d18Oprec = e18Ototal · lnf = 4‰
f=0.78 22% evaporation

## Slide 3
  Recharge by direct infiltration
    The unsaturated zone (acting like boundary layer) causing kinetic fractionation, and make the slopes much lower than the normal evaporation

## Slide 5
  Soil profiles & recharge rates

## Slide 7
  Estimating recharge with 36Cl and chloride
    Cgw = Co/R
    36Cl may be atmospheric, epigenic, anthropogenic, or hypogenic

## Slide 8
    A’Sharqiyah –sand aquifer:
      Pptn <100mL  <1% Recharge
      Co (Cl)=20ppm  ca. 1%
    Carbonate aquifers in south Oman
      Co (Cl)=10ppm.  ca, 12%
      Presence of T  thermonuclear influence?

## Slide 9
  Water loss by evaporation vs transpiration
    Transpiration: No isotopic compositional change, concentration
    Evaporation: Isotopic enrichment as well as concentration
    For the case of Nile Delta study, pan experiments gave 0.65 & 0.185‰ increase of d18O and dD, respectively, per 1% evaporation

## Slide 11: Ch.4. Groundwater
Recharge from River-Connected Aquifer
  Time-series monitoring in a river-connected aquifer

## Slide 12
  The Swiss tritium tracer experiment
    Accidental spill of 500Ci T water into a small river in Switzerland.

## Slide 13
  Water balance w/ 14C
  Recharge from the Nile River
  Recharge by desert dams

## Slide 14: Ch.4. Groundwater
Hydrograph Separation in Catchment Studies
  Two-component separation
    Qt = Qgw + Qr
    Qt·dt = Qgw·dgw + Qr·dr
    Qgw = Qt
Fig. 4-19 Storm hydrograph separation for
a two-component system using d18O

## Slide 15
  Three-component separation
    Qt = Qr + Qs + Qgw
Fig. 4-20 Storm hydrograph separation for a three-component system using d18O and dissolved silica (Si).

## Slide 16
Basin type | Rainfall (n) | Snowmelt (n)
Forest | 0.77 ± 0.17 (32) | 0.58 ± 0.18 (32)
Agriculture | 0.65 ± 0..02 (10) | 0.80 (1)
Urban | 0.02 ± 0.04 (3) | 0.51 ± 0.28 (2)
Other | 0.67 ± 0.24 (9) | 0.38 ± 0.23 (3)
Table 4-3 Summary of pre-event contribution to streamflow discharge for rainfall and snowmelt events (n) for various landuse drainage basins (from Buttle, 1994)

## Slide 17
  Example of the Big Otter Creek Basin, Ontario

## Slide 18: Ch.4. Groundwater
Groundwater Mixing
  Binary and ternary groundwater mixing
    dsample = c ·dA + (1–c )dB
Fig. 4-24 The fractional mixing of two groundwaters quantified on the basis of their stable isotope contents, shown as the fraction of groundwater "A" in the "A-B" mixture.

## Slide 19
Fig. 4-25 Ternary mixing diagram for groundwaters from crystalline rocks of the Canadian Shield. The glacial meltwater end-member was identified by the isotopic depletion observed in many of the intermediate depth groundwaters, and its 18O–Cl– composition determined by extrapolation to a 3H-free water (Douglas, 1997).

## Slide 21
  Groundwater mixing in karst systems